Effects of Berry Curvature on Thermoelectric Transport
Archisman Panigrahi
UG 4th Year
20th June 2021
Supervisor: Prof. Subroto Mukerjee, Dept. of Physics, IISc

---
Why is this interesting?
There can be a transverse Hall voltage without a magnetic field
Anomalous Hall Effect
Nernst Effect: Hall like response for a temperature gradient
Electrically insulating temperature reservoirs

---
Thermoelectric transport: Einstein and Onsager relations
- Einstein relation:
- Onsager relation:
N. R. Cooper, B. I. Halperin, and I. M. Ruzin. PRB 55 2344 (1997)
\begin{aligned} \expval{\hat{\vec{j}}_e} &= \stackrel{\leftrightarrow}{L}_{11} \cdot \left(\vec{E} + \nabla \frac{\mu}{e}\right) + \stackrel{\leftrightarrow}{L}_{12} \cdot (-\nabla{T}) \\ \expval{\hat{\vec{j}}_Q} &= \stackrel{\leftrightarrow}{L}_{21} \cdot \left(\vec{E} + \nabla \frac{\mu}{e}\right) + \stackrel{\leftrightarrow}{L}_{22} \cdot (-\nabla{T}) \end{aligned}
\vec{E} \longleftrightarrow \frac{\nabla \mu}{e}
\stackrel{\leftrightarrow}{L}_{21} = T \stackrel{\leftrightarrow}{L}_{12}
\sigma, \text{electric conductivity}
\kappa, \text{thermal conductivity}
\vec{j}_m = \nabla \times \vec{M} \color{green} \vec{j}_\text{transport} = \color{black} \vec{j}_e - \color{red} \vec{j}_M

---
Geometric phase and Berry Curvature
Time dependent Hamiltonian
Space of
Stokes’ theorem:
Like magnetic field, but in parameter space
|\varepsilon(\boldsymbol{\lambda}(t))\rangle=\color{red}e^{i \gamma(t)} \color{black} e^{-\frac{i}{\hbar} \int_{0}^{t} \varepsilon\left(\boldsymbol{\lambda}\left(t^{\prime}\right)\right) d t^{\prime}}|\varepsilon(\boldsymbol{\lambda}(0))\rangle
H(\boldsymbol{\lambda}(t))
\lambda_1, \lambda_2, \dots
\gamma = i\oint_C \bra{\varepsilon({\vec{\lambda}})}\nabla_{_{\vec{\lambda}}} \ket{\varepsilon({\vec{\lambda}})} \cdot d \vec{\lambda}
= \oint_C \vec{A}(\vec{\lambda}) \cdot d \vec{\lambda}
=\int_S \vec{\Omega} \cdot d \vec{a}
\vec{\Omega} = \nabla \times \vec{A}

---
Berry Curvature in reciprocal space
- Block wavefunctions in periodic potential
  Effective Schrodinger equation
- Crystal momentum changes with electric field
- Time evolution
u_{n, \vec{k}} \rightarrow e^{i \gamma_{_{\vec{k}}}(\Delta t)} e^{-i \frac{\varepsilon_{_{\vec{k}}} \Delta t}{\hbar}} u_{n, \vec{k}+\Delta \vec{k}}
\psi_{n, \vec{k}} (\vec{r}) = e^{i \vec{k}\cdot \vec{r}} u_{n,\vec{k}} (\vec{r})
\left[\frac{\hbar^2}{2m}(\vec{k} - i \nabla)^2 + V(\vec{r}) \right]u_{n,\vec{k}} (\vec{r}) = \varepsilon_{n,\vec{k}} u_{n,\vec{k}} (\vec{r})
\hbar \dot{\vec{k}} = -e\left(\vec{E} + \langle\dot{\vec{r}}\rangle \times \vec{B} \right)
\gamma_{_{\vec{k}}}(\Delta t) =\vec{A}(\vec{k}) \cdot \Delta \vec{k}
\vec{A}(\vec{k})=i \bra{u_{n,\vec{k}}}\nabla_{_{\vec{k}}} \ket{u_{n,\vec{k}}}

---
Construction of Bloch wavepacket, and its evolution
  Wavepacket
                  Bloch eigenfunction
\text{probability density}
\psi(\vec{r}, t=0) = \int d\vec{k} w(\vec{k} - \vec{k}_0) e^{i \vec{A}(\vec{k_0})\cdot (\vec{k} - \vec{k}_0)} e^{-i \vec{k} \cdot \vec{r}_0 } \left(e^{i \vec{k} \cdot\vec{r}} u_{n,\vec{k}}(\vec{r})\right)
\psi(\vec{r}, t=0) \underbrace{=}_? \int d\vec{k} w(\vec{k} - \vec{k}_0) e^{-i \vec{k} \cdot \vec{r}_0 } \left(e^{i \vec{k} \cdot\vec{r}} u_{n,\vec{k}}(\vec{r})\right)
\psi(\vec{r}, t=\Delta t) = \int d\vec{k} w(\vec{k} - \vec{k}_0) e^{i \vec{A}(\vec{k_0})\cdot (\vec{k} - \vec{k}_0)} e^{-i \vec{k} \cdot \vec{r}_0 } \left(e^{i (\vec{k} + \Delta\vec{k})\cdot\vec{r}} e^{i \vec{A}\cdot \vec{\Delta{k}}} e^{-i \frac{\varepsilon_{_{\vec{k}}} \Delta t}{\hbar}} u_{n, \vec{k}+\Delta \vec{k}} \right)

---
Effects of Berry curvature
        Ming-Che Chang and Qian Niu PRL 75, 1348 (1995),
        Daniel C. Ralph. arXiv: 2001.04797
- The semiclassical equation of velocity is modified
                  Decoupled
(2D)
Phase space density is modified
Anomalous velocity
(2D)
is a constant of motion
Di Xiao, Junren Shi, and Qian Niu. PRL 95, 137204 (2005)
\Delta V \left( 1 + \frac{e}{\hbar} \vec{B} \cdot \vec{\Omega} \right)
\expval{\mathcal{O}} = 2\int \frac{d\vec{k}}{(2\pi)^d} \left(1 + \frac{e}{\hbar} \vec{B} \cdot \vec{\Omega}\left(\vec{k}\right)\right) \expval{\mathcal{O}}_{_{\vec{k}}} \tilde{g}_{\vec{k}}
\begin{aligned} &\dot{r}=\frac{\frac{1}{\hbar} \frac{\partial \varepsilon}{\partial k}+\frac{e}{\hbar}(\boldsymbol{E} \times \boldsymbol{\Omega})+\frac{e}{\hbar^{2}}\left(\boldsymbol{\Omega} \cdot \frac{\partial \varepsilon}{\partial k}\right) \boldsymbol{B}}{1+\frac{e}{\hbar} \boldsymbol{B} \cdot \boldsymbol{\Omega}} \\ &\dot{k}=-\frac{\frac{e}{\hbar} \boldsymbol{E}+\frac{e}{\hbar^{2}} \frac{\partial \varepsilon}{\partial k} \times \boldsymbol{B}+\frac{e^{2}}{\hbar^{2}}(\boldsymbol{E} \cdot \boldsymbol{B}) \boldsymbol{\Omega}}{1+\frac{e}{\hbar} \boldsymbol{B} \cdot \boldsymbol{\Omega}} \end{aligned}
\begin{aligned} \dot{\vec{r}}&=\frac{1}{\hbar} \nabla_{k} \varepsilon_{k} \color{red} -\dot{\vec{k}} \times \boldsymbol{\Omega}(\boldsymbol{k}) \\ \color{black} \hbar \dot{\vec{k}}&=-e(\vec{E}+\dot{\vec{r}} \times \vec{B}) \\ \end{aligned}
\expval{\mathcal{O}} (\vec{B} = 0) = 2\int \frac{d\vec{k}}{(2\pi)^d} \expval{\mathcal{O}}_{_{\vec{k}}} \tilde{g}_{\vec{k}}

---
Boltzmann Transport framework
        Classical charge and energy currents
        Semiclassical framework
Heat current: From 1st law of thermodynamics,
\expval{\hat{\vec{j}}_e} =
\vec{j}_e = - n e v, \vec{j}_{\epsilon} &= n \epsilon v
dQ = T dS - \mu dN
\expval{\hat{\vec{j}}_Q} = 2\int \frac{d\vec{k}}{(2\pi)^d} \left(1 + \frac{e}{\hbar} \vec{B} \cdot \vec{\Omega}\left(\vec{k}\right)\right) (\varepsilon_{_{\vec{k}}} - \mu) \dot{\vec{r}}_{_{\vec{k}}} \tilde{g}_{\vec{k}}
\left\langle\hat{\vec{j}}_{Q}\right\rangle_{k}=\left\langle\hat{\vec{j}}_{E}\right\rangle_{k}-\mu\left\langle\hat{\vec{j}}_{N}\right\rangle_{k}

---
Boltzmann Transport Equation
- In equilibrium, is the Fermi distribution.
- The external fields are small, and it deviates slightly from
  the Fermi distribution
- The system tries to attain equilibrium, with a relaxation time
- We assume that the more the distribution deviates, the faster it would try to return to equilibrium, relaxation time approximation.
\tilde{g}_k
\tilde{g}_k = f_k + g_k
\tau \sim 10^{-14} s
D_t \tilde{g}_k = -\frac{\tilde{g}_k - f_k}{\tau}
D_t \equiv \frac{\partial}{\partial t} + \dot{\vec{k}}\cdot\frac{\partial}{\partial \vec{k}} + \dot{\vec{r}}\cdot\frac{\partial}{\partial \vec{r}}
f_{_{\vec{k}}} = \frac{1}{e^{\beta \left(\varepsilon_{_{\vec{k}}} - \mu \right)} + 1}

---
Boltzmann Transport Equation
In steady-state, and homogeneous fields, the equation in becomes,
- Why is the perturbation theory valid?
  Dimension analysis: this term = the first term, is the cyclotron frequency
- This is less than the first term when
- If then the critical field is ~ 570 T
Why even consider this term, then??
\boxed{\frac{g_k}{\tau} -\underbrace{\frac{\frac{e}{\hbar^2} \frac{\partial \varepsilon}{\partial \vec{k}} \times \vec{B}}{1 + \frac{e}{\hbar} \vec{B} \cdot \vec{\Omega}} \cdot\frac{\partial}{\partial \vec{k}} g_k}_{\text{treated as a perturbation}} = \frac{\partial f}{\partial \varepsilon}\frac{1}{1 + \frac{e}{\hbar} \vec{B} \cdot \vec{\Omega}} \frac{1}{\hbar} \frac{\partial \varepsilon}{\partial \vec{k}}\cdot\left[e \vec{E} + \nabla{\mu} + \nabla T \frac{\varepsilon - \mu}{T}\right]}
\omega_c \tau \times
\omega_c = \frac{e B}{m^*}
B < B_{critical} = \frac{m^*}{e\tau}
m^* \sim m, \tau \sim 10^{-14} s

---
Boltzmann Transport Equation
In steady-state, and homogeneous fields, the equation in becomes,
Einstein and Onsager
Relations are satisfied
The solution, with
\boxed{\begin{aligned} g_k &= \frac{\partial f} {\partial \varepsilon}\frac{1}{1 + \frac{e}{\hbar} \vec{B}\cdot\vec{\Omega}} \frac{\tau}{\hbar} \frac{\partial \varepsilon}{\partial \vec{k}}\cdot \vec{S} \\ & + \frac{\frac{e \tau}{\hbar^2} }{1 + \frac{e}{\hbar} \vec{B}\cdot\vec{\Omega}} \frac{\partial \varepsilon}{\partial \vec{k}} \cdot \vec{B} \times \left[ \frac{\partial}{\partial \vec{k}} \left[ \frac{\frac{\partial f} {\partial \varepsilon} \tau}{1 + \frac{e}{\hbar} \vec{B}\cdot\vec{\Omega}} \right] \frac{\vec{S}}{\hbar} \cdot \frac{\partial \varepsilon}{\partial \vec{k}} + \frac{\frac{\partial f} {\partial \varepsilon} \tau}{1 + \frac{e}{\hbar} \vec{B}\cdot\vec{\Omega}} \left[\left(\frac{1}{\hbar} \vec{S}\cdot \frac{\partial }{\partial \vec{k}} \right)\frac{\partial \varepsilon}{\partial \vec{k}} \right] \right] \right] \end{aligned} }
\boxed{\frac{g_k}{\tau} -\underbrace{\frac{\frac{e}{\hbar^2} \frac{\partial \varepsilon}{\partial \vec{k}} \times \vec{B}}{1 + \frac{e}{\hbar} \vec{B} \cdot \vec{\Omega}} \cdot\frac{\partial}{\partial \vec{k}} g_k}_{\text{treated as a perturbation}} = \frac{\partial f}{\partial \varepsilon}\frac{1}{1 + \frac{e}{\hbar} \vec{B} \cdot \vec{\Omega}} \frac{1}{\hbar} \frac{\partial \varepsilon}{\partial \vec{k}}\cdot\left[e \vec{E} + \nabla{\mu} + \nabla T \frac{\varepsilon - \mu}{T}\right]}
\vec{S} =e \vec{E} + \nabla \mu + \frac{\varepsilon - \mu}{T} \nabla T

---
Which all terms contribute
2nd order
0, as it should be without any external field
For a filled band,
Chern number, integer
Independent of scattering!!
\expval{\hat{\vec{j}}_e} = -e \int \frac{2 d\vec{k}}{(2\pi)^2} ({f}_{\vec{k}} + {g}_{\vec{k}}) \left[\frac{1}{\hbar} \frac{\partial \varepsilon_{_{\vec{k}}}}{\partial \vec{k}} + \frac{e}{\hbar} (\vec{E}\times\vec{\Omega}(\vec{k}))\right]
\expval{\hat{\vec{j}}_e} = -e \int \frac{2 d\vec{k}}{(2\pi)^2} \left[{f}_{\vec{k}} \frac{e}{\hbar} (\vec{E}\times\vec{\Omega}(\vec{k})) + {g}_{\vec{k}} \frac{1}{\hbar} \frac{\partial \varepsilon}{\partial \vec{k}}\right]
\expval{\hat{\vec{j}}_e}_{anomalous} = - 2 \frac{e^2}{h} \vec{E} \times \int_{\text{filled}} \frac{d\vec{k}}{2\pi} \vec{\Omega}(\vec{k})

---
Which all terms contribute
- For a filled band,
- This is not the (usual) quantum Hall effect
Independent of scattering!!
\expval{\hat{\vec{j}}_e} = -e \int \frac{2 d\vec{k}}{(2\pi)^2} \left[{f}_{\vec{k}} \frac{e}{\hbar} (\vec{E}\times\vec{\Omega}(\vec{k})) + {g}_{\vec{k}} \frac{1}{\hbar} \frac{\partial \varepsilon}{\partial \vec{k}}\right]
\expval{\hat{\vec{j}}_e}_{anomalous} = - 2 \frac{e^2}{h} \vec{E} \times \int_{\text{filled}} \frac{d\vec{k}}{2\pi} \vec{\Omega}(\vec{k})
\sigma_{xy} = -\sigma_{yx} = \frac{2 e^2}{h} \mathcal{C}

---
Issue
(Nernst)
- Apparently, a temp gradient or
  a chemical potential gradient
  cannot give rise to anomalous Hall effect
- No term like and
☹️
☹️
☹️
- What we missed:
- The wavepackets are not localized
- Circulating magnetization currents
Orbital magnetic moment
Di Xiao, Yugui Yao, Zhong Fang, and Qian Niu. PRL 97, 026603 (2006)
\vec{m}_{{k}} = -\frac{e}{2 m} \bra{\psi_{{k}, {r}_0}}(\hat{\vec{r}} - \vec{r}_0)\times\hat{\vec{p}}\ket{\psi_{{k}, {r}_0}}
\nabla \mu \times \vec{\Omega}
\nabla T \times \vec{\Omega}

---
Wavepackets are not localized
\expval{\hat{O}} ( \text{ } ) =

---
To calculate electric current, we use
Similarly, for heat current
\hat{O} = \frac{-e \hat{p}}{m}
\expval{\hat{\vec{j}}_Q} = \int \frac{2 d\vec{k}}{(2\pi)^d} (\varepsilon_0(\vec{k}) - \mu) \left[ {g}_{\vec{k}} \frac{1}{\hbar} \frac{\partial \varepsilon_0(\vec{k})}{\partial \vec{k}} + \frac{e}{\hbar} {f}_{\vec{k}} (\vec{E}\times\vec{\Omega}(\vec{k}))\right] \color{red} - \vec{E} \times \int \frac{2 d\vec{k}}{(2\pi)^d} f_{\vec{k}} \vec{m}_{\vec{k}}
\left. \expval{\hat{\vec{j}}_e}\right|_{\vec{B} = 0} = -e \int \frac{2 d\vec{k}}{(2\pi)^d} {g}_{\vec{k}} \frac{1}{\hbar} \frac{\partial \varepsilon_0({{\vec{k}}})}{\partial \vec{k}} + {f}_{\vec{k}} \frac{e}{\hbar} (\vec{E} \times \vec{\Omega}(\vec{k})) + \color{red} \nabla \times \int \frac{2 d\vec{k}}{(2\pi)^d} f_{\vec{k}} \vec{m}_{\vec{k}}

---
Effects of orbital magnetization
Energy eigenvalues are modified
Net magnetization can be obtained from the Free energy
\varepsilon_{_{\vec{k}}} = \varepsilon_0(\vec{k}) - \vec{m}_{_{\vec{k}}} \cdot \vec{B}
\begin{aligned} G &= -\frac{1}{\beta} \sum_{\vec{k}} \log(1 + e^{-\beta(\varepsilon_{_{\vec{k}}} - \vec{m}_{\vec{k}}\cdot \vec{B} - \mu)}) \\ &= -\frac{1}{\beta} \int \frac{d\vec{k}}{(2\pi)^d} \left(1+\frac{e}{\hbar} \vec{B}\cdot\vec{\Omega}\right) \log(1 + e^{-\beta(\varepsilon_{_{\vec{k}}} - \vec{m}_{\vec{k}}\cdot \vec{B} - \mu)}) \end{aligned}
\vec{M}^e = -\left.\frac{\partial G}{\partial \vec{B}}\right|_{\vec{B}=0} = \frac{1}{\beta} \int \frac{2 d\vec{k}}{(2\pi)^d} \color{red} \frac{e}{\hbar} \vec{\Omega}(\vec{k}) \log(1 + e^{-\beta(\varepsilon_0(\vec{k}) - \mu)}) \color{black} + \int \frac{2 d\vec{k}}{(2\pi)^d} f \vec{m}_{\vec{k}}

---
Transport current
Now we are ready to calculate the transport current
\boxed{\begin{aligned} \color{green}{{\vec{j}}^e}_{\text{transport}} &= \color{black}\expval{\hat{\vec{j}}_e} \color{blue} - {\vec{j}^e}_{M} \\\color{black} &= \int \frac{2 d\vec{k}}{(2\pi)^d} (-e){g}_{\vec{k}} \frac{1}{\hbar} \frac{\partial \varepsilon_0({{\vec{k}}})}{\partial \vec{k}} - {f}_{\vec{k}} \frac{e^2}{\hbar} \left(\left[\color{orange} \vec{E} + \frac{\nabla \mu}{e} \color{black}\right] \times \vec{\Omega}(\vec{k})\right) \\ &- \frac{\nabla T}{T} \times \color{red} \int \frac{2 d\vec{k}}{(2\pi)^d} \frac{e}{\hbar} \vec{\Omega}(\vec{k}) \left[f_{\vec{k}} (\varepsilon_0(\vec{k}) - \mu) + k_B T \log(1 + e^{-\beta(\varepsilon_0(\vec{k}) - \mu)})\right] \end{aligned}}

---
How about Onsager relation?
We can define energy magnetization,
Di Xiao, Yugui Yao, Zhong Fang, and Qian Niu.
PRL 97, 026603 (2006)
☹️
N. R. Cooper, B. I. Halperin, and I. M. Ruzin. PRB 55 2344 (1997)
\vec{M}^E = \vec{M}_0^E + \underbrace{\phi(\vec{r})}_\text{electric potential energy} \vec{M}^N
\boxed{\begin{aligned} \vec{j}_{\text {transport }}^{Q} &=\vec{j}_{\text {transport }}^{E}-\mu \vec{j}_{\text {transport }}^{N} = \vec{j}_{\text {transport }}^{E}-\frac{\mu}{-e} \vec{j}_{\text {transport }}^{e}\\ &=\int \frac{2 d\vec{k}}{(2\pi)^d}(\varepsilon_0(\vec{k})-\mu) \frac{1}{\hbar} \frac{\partial \varepsilon_0(\vec{k})}{\partial \vec{k}} g_{k} \\ &+\vec{E} \times \color{red} \int \frac{2 d\vec{k}}{(2\pi)^d} \left[(\varepsilon_0(\vec{k})-\mu) \frac{e}{\hbar} \vec{\Omega} f_{k} + k_{B} T \frac{e \vec{\Omega}}{\hbar} \log(1 + e^{-\beta(\varepsilon_0(\vec{k}) - \mu)})\right] \\ &\color{black} + \int \frac{2 d\vec{k}}{(2\pi)^d} (-\mu) \frac{1}{\hbar} \nabla \mu \times \vec{\Omega} f_{k} \\ &-\frac{\mu}{\hbar} \int \frac{2 d\vec{k}}{(2\pi)^d} \frac{\nabla T}{T} \times \vec{\Omega}\left[f_{k}\left(\varepsilon_0(\vec{k})_{k}-\mu\right)+k_{B} T \log(1 + e^{-\beta(\varepsilon_0(\vec{k}) - \mu)})\right] \\ &-\nabla \mu \times \frac{\partial \vec{M}_{0}^{E}}{\partial \mu}-\nabla T \times \frac{\partial \vec{M}_{0}^{E}}{\partial T} \end{aligned}}

---
Possible resolution
\boxed{-\frac{\partial \vec{M}_{0}^{E}}{\partial \mu}=\int \frac{2 d\vec{k}}{(2\pi)^d} \frac{ \vec{\Omega}}{\hbar} \left[\varepsilon_0(\vec{k}) f_{k} + k_{B} T \log(1 + e^{-\beta(\varepsilon_0(\vec{k}) - \mu)})\right]}

---
Berry curvature and Chern numbers of some microscopic
models
In a two band system with Hamiltonian
Monolayer graphene
Non-zero Berry curvature when there is a finite band gap : Spin-Orbit Coupling
However, there is Time Reversal Symmetry, so
H = d_x \sigma_x + d_y \sigma_y + d_z \sigma_z
\Omega_z = i \int d\vec{r} \nabla_{\vec{k}_x} u_{\vec{k}}^* \times \nabla_{\vec{k}_y} u_{\vec{k}} = \frac{1}{2} \hat{d} \cdot \left(\frac{\partial \hat{d}}{\partial k_x} \times \frac{\partial \hat{d}}{\partial k_y} \right)
\vec{\Omega}(\vec{k}) = -\vec{\Omega}(-\vec{k}), \mathcal{C} = 0
\Delta = 10^{-3} m eV

---
Valley Polarization
Electrons can be made to selectively occupy valleys with circularly polarized light
A. Friedlan and M. M. Dignam PRB 103, 075414 (2021)

---
Bilayer Graphene
- We can generate a band gap by applying an electric field

---
Results for valley Chern number
H(\vec{k}) = k_x \sigma_x + k_y \sigma_y + \alpha (k_x^2 + k_y^2)^n \sigma_z

---
New results
The condition on the energy magnetization for Einstein relation to hold for anomalous Heat current
Solution of Boltzmann transport equation upto linear order, that captures the effects of Berry curvature in regular Ohmic, regular Hall and regular Nernst effects

---
Thank you